I	CLIMATE CONDITIONS

I.1  	Provide the relevant number(s) of heating degree days for the country. Provide this figure according to a base indoor temperature of 18(C or according to standards of your country (specify them). When there is a change from the previous survey please provide an explanation for that change. Take into account relevant regional climatic variations.

The heating season in Lithuania lasts 6-7 months per year. Heating degree-days are set by the norms of Building Climatology (1995). The maximum heating degree-days in Lithuania are 4081 and the minimum – 3445. For example, in Vilnius: heating degree-days are 4005 (during a season) when average temperature of a day is lower then +10 0C; 3815 - +8 0C; 2664 - 00C.

I.2	Provide the average indoor temperature. Please provide the values used in your country.

The average (recommended) indoor temperatures during heating season are set by sanitary norms HN 42:2004 “Microclimate of residential and public buildings” (2004). For example: Type of premises Indoor temperature 0C 1. Residential buildings 18-22 2. Commercial buildings 20-22 3. Day nursery 21-23 4. Kindergartens 20-22 5. Schools, universities 18-19 6. Hospitals, health centres 19-21

I.3	Provide a short description of the climatic conditions in your country (including regional climatic variations).

The Lithuanian climate is affected by global factors and local geographical conditions. The major impact is done by the geographical position of Lithuania, because it is located in northern part of the middle latitude climate zone. According to B. Alisov classification, Lithuania is attributed to the south-western sub area of the Atlantic continental forest area. Only the Lithuanian Baltic Sea coast climate is close to the Western Europe climate and could be ascribed to the separate climate sub area of the Southern Baltics. The biggest impact upon the Lithuanian climate is done by the Atlantic Ocean, as well as the mild waters of the Golf Stream, washing the western coasts of Europe. Most often the Lithuanian climate is affected by the air front of the middle latitude (80-87%): more often continental in spring and summer, and sea air front in autumn and winter season. More seldom Lithuania is reached by arctic weather (6-17%) and very rarely by tropical (1-2%) weather. The average annual temperature in Lithuania equals to 6,2C degrees. The difference between the warmest July month and the coldest January month is 21,8º C. Sometimes in summer the temperature may reach 30C degrees, as well very low temperatures – e.g. -20°C - can occur in winter season, and up to -30°C during the nighttime (Fig. 1). Due to storms, squalls and rain, the biggest volume of precipitation falls in summer period (up to 50% of annual precipitation amount). The lowest volume of precipitation falls in spring time, because at that time mostly anticyclones dominate. Month Jan Feb Mar Apr May Jun Jul Aug Sep Oct Nov Dec Heat records +12,6 +16,5 +21,8 +28,8 +34,0 +35,0 +37,5 +36,0 +32,0 +26,0 +18,0 +15,6 Cold records -40,5 -42,9 -37,5 -23,0 -6,8 -2,8 +0,9 -2,9 -6,3 -19,5 -23,0 -34,0 Fig. 1. The records of temperature in Lithuania (oC). Fig. 2. Annual outdoor temperature in Vilnius over 1778-2007 years. Fig. 3. Deviations from normal annual outdoor temperature in Lithuania.

II	DISTRICT HEATING

II.1	Provide the following key figures for 2007. (*- Only LDHA members data)

To make it clearer, let me remind you that the entire information provided in the present questionnaire was extracted from the data base of our association, i.e. in total there are 39 heat supply companies in Lithuania and 32 of them are the members of the Lithuanian District Heating Association. These companies produce and supply 98 % of the total heat energy volume, transmitted by Lithuanian district heating networks.

| Number of DH utilities in your country. (The Association is comprised of 41 members 32 are DH companies. Members of LDHA produce and supply around 98 % of the total heat through the DH network in the Republic of Lithuania, and 9 companies whose activities are closely linked to the heat sector.) | 32 |
| --- | --- |
| Total installed DH capacity in your country (in MWth) (Only LDHA members data) . | 8263,3 |
| Total length of the pipeline network (in km) *. | 2458,1 |
| Indication of the annual turnover in the DH sector of your country (in bln euro or local currency). * | 317 mio. EUR |
| Estimation of employment figures in the DH sector of your country. * | In 2007 year there were 4941 employments in the DH sector |
| Estimated number of residents heated by DH in your country (in persons and/or households). * | In Lithuania there are about 28000 biuldings (including 17500 apartments houses) connected to DH. |
| District heated floor space in your country (in m2). * | About 34 000 000 |
| Provide the heat sales volume for new connections to DH in your country for 2007 (in GJ). * Estimate the corresponding number of new persons/households connected and the additional heated floor space (in m2). * | ~ 849600 GJ less then 2006 year. ~ 500 new apartments houses where connected over 2007 year in DH and it’s about 2100000 m2 |

II.2	 Provide the total DH delivery for 2007.

| Sector | In GJ |
| --- | --- |
| Residential sector * | In 2007, 28677,6 TJ of district heat was delivered to final consumers out of which 20779,2 TJ was delivered to households for heating and hot water preparation purposes. The rest (about 27,5 %) was delivered to other users (industry, commercial and public services). |
| Services and other sector * |  |
| Industrial sector * |  |
| TOTAL* |  |

II.3	Provide the energy supply composition for district heat generated. Provide the overall picture of the energy sources used for heat generation. Do not take into account any ownership / contractual arrangements in case heat is bought from a third party.

|  | 1997 | 2002 | 2007 |
| --- | --- | --- | --- |
| Source | In GJ | In % | In GJ | In % | In GJ | In % |
| In cogeneration | we have no data |  |
| Coal and coal products |  | 0 |
| Oil and petroleum products |  | 1,1 |
| Natural gas |  | 44,8 |
| Nuclear |  | 0 |
| Combustible renewables |  | 3,2 |
| Waste |  | 0 |
| Renewables |  |  |
| Geothermal |  | 0,2 |
| Combustible renewables |  | 13,0 |
| Solar, wind and other |  | 0 |
| Waste |  | 0 |
| Heat pumps |  | 0 |
| Industrial surplus heat |  | 0,2 |
| Coal and coal products |  | 0,5 |
| Natural gas |  | 32,8 |
| Oil and petroleum products |  | 4,2 |
| Nuclear |  | 0 |
| Electricity |  | 0 |
| TOTAL |  | 100 |  | 100 |  | 100 |

I.4	Comment the development of fuel use for DH over the last 10 years with the use of data or graph if available.

1. Fuel use for DH over 1997-2007 years. 2 Fig. Fuel use for DH over 1990-2007 years. As we can see from Fig. 1 and 2, the main fuel until 2001/2002 was natural gas and heavy fuel oil, whereas other types of fuel comprised only <10 percent of the total amount. After year 2002 the consumption of HFO decreased, step by step replaced by natural gas and bio fuel. The use of fuel types was mostly influenced by the following two factors: price difference and pollution reduction requirements. Due to the decrease of natural gas prices in the period of 1997–1998, the consumption of HFO decreased as well, increasing the consumption of natural gas. On the other hand, that was also influenced by the environmental protection requirement to decrease the atmosphere pollution. The industrial companies had to reduce the consumption of HFO due to its high sulphur content. Low-sulphur HFO can be purchased from Western European countries, but it is rather expensive and up till now it is not purchased for this reason. Therefore in the latest years only natural gas (imported from abroad), bio fuel and other renewable energy sources, available in Lithuania, are used.

II.5	Provide the average CO2 emissions per MJ of district heat generated (for 2007).

0,17 kg co2/MJ

II.6	Provide a description (with the use of data) of the development of DH during the last five years (2002-2007). Mention developments in the residential, service and other and industrial sectors.

Production and consumption of heat. The variations in this sector can be explained by sudden changes in the heat consumer structure and heat energy saving in the presence of increasing heat prices. We can see from the heat energy analysis 1990 - 2007 (Fig. 1), that almost no consumers of DH steam are left any longer. This is related to the restructuring of industrial plants. The consumption market has changed, resulting in liquidation of large-scale plants, because their production became unsaleable. As well, the economic blockade of 1992–1993 had a huge impact upon the consumption of heat energy, and this can be clearly seen in Fig. 1. Fig. 1 heat energy analysis 1990 - 2007 Starting from year 2000, the consumption of district heating energy got more or less stable and is still increasing. We have to state, that inhabitants of dwelling houses became the main consumers of the heat energy. As well, we have to emphasize the fact, that the decrease of heat energy transmission losses can be clearly observed. This is illustrated by Fig. 2 – in 2006 the heat energy losses decreased by 17,78 percent and are still diminishing. Fig. 2. Heat energy balance over 1990-2006 years. Besides, a very important indicator is the comparative fuel costs, that in 2006 decreased to 98,3 kg for the generation of 1MWh. Nowadays, the heat energy generation sources are divided into the following 2 groups: the sources producing ≥5 GWh of heat energy annually; the sources producing less than 5 GWh of heat energy annually. District heating networks. As we can see from Fig. 1, after the consumption of DH steam has considerably decreased, this affected the length of steam and condensate pipelines in total balance of DH supplies. The alterations of DH superheated water, steam and condensate pipelines over 1991–2006 years are provided in Fig. 3 (columns ”Total“ include the network length, excluding the non-balance pipelines). Fig 3. The alterations of DH superheated water, steam and condensate pipelines over 1991–2006. It was mentioned herein before, that after the liquidation of large-scale industrial plants, which used to employ huge amount of steam, the steam demand has considerably diminished. Therefore, it was necessary to decommission the large-scale steam supply and condensate pipelines, because technologically wise it became impossible to supply low amount of steam, as well as not profitable from the economical point of view, and over 1993 – 2007 years resulting in the length reduction of steam and condensate pipelines by >4 times, i.e. up to 33,7 km. Nowadays, the consumers of steam, except those located adjacent to heat generation utilities, are supplied with steam by installing individual steam generation sources. As per the erection dates of the DH networks (see Fig. 4), we have to admit that most of them were constructed before year 1991. Fig 4. The length of DH networks as per the erection date. Following the design practice that existed at that time, and what can be clearly seen now from the actual consumption during that period, the demand for the district heating energy and especially for the hot water preparation was calculated to a lot higher volume than it was necessary. The comparison results of the installed capacity and the highest demanded capacity in year 1999, are displayed in Fig. 5. Fig 5. The installed and the highest demanded capacity values: HC – for district heating and cooling; HW – for hot water. For this reason, the designed permeability of district heating pipelines is not fully exploited. Therefore, it is possible to make a conclusion, that too big diameters of pipelines increase the heat losses, as well. Taking into account the heat losses due to the worn-out heat insulation, it would be necessary to reconstruct the existing pipelines or at least to replace the heat insulation with a new one, but from the economical point of view it is dot feasible due to very high investment costs. Therefore for the same reason, currently only worn-out pipelines are being reconstructed, and new pipelines are being erected for the provision of heat to the new-constructed objects only. This can witness the low volume of new district heating pipelines constructed during the recent years. As well, we have to have in mind that after the year 2000 mostly pre-insulated pipes are used for the construction of new DH networks, as well as applying the most modern – non-channel technology. The data on the diameters of the DH pipelines is provided in Fig. 6. Fig. 6. The data of pipeline diameters. Residential sector. As we can see above from Fig. 1, the residential sector became the main consumer of the district heating energy. During the last 5 years, the structure of the district heating consumers is not changing (see Fig. 7). Fig. 7. The consumers of district heating energy. Fuel and its prices. Fuel prices have a huge impact on the consumption of the district heating energy and the development of DH networks, because the fuel price constitutes about 80 percent of the heat price. The alterations of fuel prices in the period of 1990–2006 and other related data are provided in Fig. 8. Fig. 8. The alterations of fuel prices, used mostly for the DH energy generation in 1996–2007. From Fig. 8 we can see, that approximately until 2004 the heavy fuel oil prices altered only slightly and the average price remained rather the same. In 1999–2000 the natural gas price dropped considerably, but started increasing later on, and in year 2001 it already exceeded the prices existing in 1996. Slightly altering they remained similar until 2005. Bio fuel price did not change until year 2001. Further on, starting from 2004, the HFO price started growing up rapidly. One year later, i.e. starting from year 2005, the natural gas price reached the price of HFO, because the prices were linked together. From year 2003, the bio fuel prices increased, because the demand for bio fuels in the heat generation sources has increased. Besides, the demand for timber in the furniture industry and exports increased as well. From 2005 to 2007 the natural gas and HFO prices for heat generation companies has considerably increased, i.e. in 2007 the natural gas and HFO prices accordingly increased by 83% and 98%, compared to year 2005, whereas as the bio fuel price increased at the same period only by 55%. Heat prices and consumer debts. The alteration of heat prices over 1990 – 2007 years are provided in Fig. 9. Fig. 9. The price alterations of the DH energy supplied over 1990–2007 years. The constant increase of DH prices is related to the following factors: increasing fuel prices, technological equipment prices, labor costs and other expenses. One of the related and very important factors is constant consumer debts for the delivered DH energy. The volume of the consumer debts is illustrated in Fig. 10. Fig. 10. Consumer debts over 2001–2007 years. In 2002 the total amount of the consumer debts equaled to over 213 million Litas. The positive fact is that by the end of the year 2006, the consumer debts decreased by almost 100 million Lt – up to 127 million Lt. If we look at the breakdown of debts according to the consumer groups, we can see that the residents comprise the biggest debt group. The consumer debts decreased slightly over 2006/2007, but still they constitute 76 percent of the total volume of debts. d

II.7	Provide an assessment of the existing driving forces and/or opportunities that favour an expansion of DH. Include in the description elements like national legislation, taxation, competition, building codes, policy/administrative priorities, investment aspects, organizational capacity, culture etc.

Heat sector is one of the key energy subsectors in Lithuania. Its activity is closely related to other energy industries, such as power, gas, oil and renewable energy sources. Much has been done in all the fields of the district heating sector over the previous (1996-2007) period: Eliminated group boiler houses and installed automatic heat stations in multiflats, dwelling-houses and other buildings; Implemented record on how much of heat was produced and supplied to the network and how much of heat was sold for the consumers. The difference evaluates the loss of heat in the network. In the heat production sources installed boilers adapted to burn biofuel (~360 items; power ~610); installed condensational economizers in boilers (18 units of 20 MW economizers have been installed from year 2004; in the future 15 units of 32 MW economizers are planned to be installed throughout Lithuania); Replacements of pipelines and optimization of network when uneconomical consumers are disconnected and they are erected local boiler houses; In the sources of heat production were erected cogeneration equipments in order to produce electricity. Throughout the 18 years of independence there have been built/modernized 13 cogeneration plants in Lithuania. The biggest of them are as follows: II Vilniaus elektrinėje (2006 m.), AB “Panevėžio energija” (2008), UAB „Litesko“ filialuose: „Marijampolės šiluma“ (2007 m.), “Alytaus energija” (2008), Noreikiškių katilinėje (2006 m.), UAB „Tauragės šilumos tinklai“ (2007 m.). The total electricity and thermal power installed in these power plants is 62 MW and 153 MW respectively. The erection of new pipelines and connection of new consumers (dwelling-houses, administration and office buildings, shops, etc.); The replacement of existing boiler burners with the new ones in order to minimize pollution and increase economy; The education of inhabitants, other consumers, municipalities and state institution officers on the advantages of district heating. In January 2007, the Seimas of the Republic of Lithuania approved the new National Energy Strategy providing for the extensive development of the district heating in Lithuania. Wider application of local fuel and municipal waste, installation of cogeneration power stations, modernisation of the heating system, building interior heating system and forced hot-water system, also the warmth-keeping of buildings will allow to reduce heat consumption and at the same time the cost sustained by residents. From 1996 to 2006 some LTL 1 billion were invested into the heat sector. However, the investment of more than LTL 9 billion will be required for the renovation of the heat economy sector over the next fiveyears,asprovidedinthe 2008-2012 action plan for the implementation of the National Energy Strategy approved by the Government of the Republic of Lithuania on 27 December 2007. The main institutions managing the Energy sector are: 1) the Government or its authorised institution; 2) the Ministry of Economy; 3) the Ministry of the Environment; 4) municipalities. The main Law regulating the energy sector is The Energy Law (adopted in October, 2002) is the main legal act on Lithuanian energy system regulation. Under this law there are 6 other laws, which regulate main energy sectors: power, heat, natural gas, oil, nuclear energy and renewable resources: Low on Energy Heat Law Natural Gas Law Law on Electricity Law on Biofuel, Biofuels for transport and Bio-oils Law on State Stocks of Petroleum Products and Crude Oil Law on Nuclear energy The main strategiс documents: National Energy Strategy (1994, 1999, 2002, 2007) Implementation Plan of National Energy Strategy 2008-2012 (2008) National Energy Efficiency Programme 2006-2010 (2006) Energy Efficiency Action Plan (2007) Housing Strategy (2004) Support Programme on Renovation of Multy-family Apartment Houses (2004, 2008) National Strategy on Sustainable Development (2003) Guidelines of District Heat Sector Development (2008) Programme for the promotion of biofuel production and use (2004) State Strategy Plan on Waste Disposal (2007) National Lisbon strategy implementation programme (2007) DH legislation The heat sector is managed by the Heat Law adopted in May, 2003. The law regulates the activity of subjects of economy acting in the heat sector, their relationship with heat consumers, their interrelationship and responsibilities. The general objectives: to guarantee the reliable and high quality least-cost heat supply to consumers. to establish the reasonable competition in the heat sector. to defend the rights and legitimate interests of heat consumers. to improve the efficiency of heat production, transmission and consumption. to increase the utilization of local fuel, biomass and renewable energy resources in heat production; to reduce the negative impact of heat energy industry on the environment.

II.8	Provide an assessment of the existing barriers to the expansion of DH and describe the challenges DH faces for the period to come. Include in the description elements like national legislation, taxation, competition, building codes, policy/administrative priorities, investment aspects, organizational capacity, culture etc.

Market/institutional barriers Ignalina NPP generates about 80% of total electricity per year. The final closure of Ignalina NPP will have direct socio-economic, environmental and other consequences: the electricity price will grow for whole population; big investment will be required for modernisation of power capacities and construction of alternative electricity generating sources which would replace the existing production of NPP. The policy of gas pricing that determines the gas price level for the consumers according to the amount of gas consumed is not market based and distorts the market. Adverse effect on the process of liberalization of the natural gas market was made by the situation of competition in the non-regulated gas market – the eligible customers could chose only among two suppliers – AB “Lietuvos Dujos” and UAB “Dujotekana”, which were buying gas from the sole external supplier – AAB “Gazprom” and each had pre-set gas quota; thus no competition exists between them. Eligible consumers (which are the major DH companies producing about 90% of heat in DH market)) are discriminated. For ex., independent gas supplier Dujotekana UAB uses a sales price margin of more than 30%. Therefore, currently Lithuania faces the situation where eligible customers pay for the gas more than the regulated ones. The regulation of supply prices is essential in order to avoid extortionate prices. The gas price level directly influence the district heat price as the share of natural gas makes about 83% in the general fuel balance for DH production. Electricity and gas networks have no direct connections to the energy systems of Western Europe, thus, they are dependant on a single supplier of natural gas (Russia) and have no opportunities to integrate into the power systems of Western and Central European countries. Insufficient growth and uneven distribution of investments by regions of the country. The share of renewable and indigenous energy resources in the primary energy balance are increasing but their potential has so far not been sufficiently used. Indebtedness of heat consumer: in the end of 2007, the total debt of the heat users makes about 11 % of annual revenue of DH companies. Inhabitants are the main debtors (about 75% of the debt sum). In order to decrease the amount of expenditures, the State subsidies for heat and hot water are applied to consumers with low incomes from 1996. The environmental taxes are unevenly distributed. The owners of small boilers heating individual houses or multi-storey buildings do not pay environment taxes, while DH companies usually do. These taxes influence the overall costs as well. Recalculation of DH price is not related to increase of fossil fuel price, thus DH companies are brought to loss. Uncoordinated pricing principles between the country’s energy sectors. The result of uncoordinated pricing principles in 2007 year was ~ 32 mio.EUR. loss of Heat sector. The procurement cost of electricity energy generated in biofuel power plants is lower than the cost of electricity energy of some power plants which use fossil fuel (SC „Lietuvos elektrinė“ is given priority anticipating to increase the procurement cost until 9,86 €c/kWh, when the the procurement cost for biofuel power plants is only 8,7 €c/kWh (new 8,7 €c/kWh price will be beginning with 2009 year). Because of bureaucracy, state and municipal institutions do not issue permissions for the construction of cogeneration power plants burning municipal waste. Such power plants would generate electricity and heat for consumers. There is a risk that the EU financial support for 2007-2013 will not be fully employed or misused. As 2 years have passed, however, estimated instructions concerning EU structural support as regards the implementation of modernizing means in heating sector have still not been confirmed. In 1997 DH companies were transferred to the jurisdiction of the local municipalities, tremendous debts of JSC “Lietuvos Energija” (about 415 million LTL) were transferred as well and the repayment of this debt also put high pressure on the DH suppliers. Housing maintenance problem: no sufficient attention was paid to the establishment of an institutional and legal system for housing maintenace. Only 17% of the total number of apartment buildings are managed and maintained by the housing owners who establish home owners associations. When establishing home owners' associations, the owners often lack initiative, as well as information and organisational-technical support by the public and local government institutions. Home owners' associations usually are not able to ensure appropriate maintenance of common ownership in the multi-apartment buildings. They can contract maintenance companies operating on the market, however, shortage of companies providing good quality services is noticed. About 70% of Lithuanian population resides in multi-family apartment houses. These houses without proper maintenance depreciated. Meantime up to 90 % of housing stock needs to be renovated in Lithuania. Insufficient State attention for solving this problem still exists. In 2004 The State Support Programme on Renovation of Multi-family Apartment Houses was adopted. However this support mechanism is still inefficient and has no driving force. According to the data provided by the Ministry of Environment there are 700 partially renovated apartment houses. It makes only 2 % of all 45000 apartment houses, where reside the majority of Lithuanian population. Society has not yet realized the importance of energy consumption efficiency. The Green Energy is not considered the worth among society. The awareness of society on building renovation and energy efficiency issues should be increased.

II.9	Provide an assessment of the existing training opportunities for future professionals in the DH sector of your country.

Energy specialists in Lithuania are educated at Vilnius Gediminas Technical University, Kaunas Technological University, Vilnius University and several more higher but non-university schools (Vilnius Technological and Design College, etc..). Besides, in Lithuania we have the most modern in the Baltic States Energy Specialists Training Centre. Developing the skills of energy specialists, the LDHA continuously participate in national and international conferences, produce reports on district heating issues, organize seminars, form specialist groups and co-ordinate their meetings. We are actively involved in the drafting, consideration and improvement of the Lithuanian laws and subordinate legislation related to the development and management of the district heating sector. LDHA Care is taken about the qualification and training of the staffofthe Association enterprises Project for 2001-2004 financed by the Danish Energy Agency In 2001-2004, financing was provided from the Danish environmental energy sector programme supporting the Lithuanian district heating sector for the implementation of project Training Network of for Staff Engaged in the Lithuanian District Heating, 2001. The goal of the project was to provide assistance to the LDHA by developing the Lithuanian district heating sector and by strengthening the Association itself. The goal was implemented as follows: By strengthening the image of the DH sector and the political role of the LDHA, by expanding co-operation with various competent authorities; By developing and implementing training programmes for the staffofLDHAenterprises; By preparing technical guidelines. In the spring of 2002 the LDHA (jointly with Swedish DH Council SweHeat) organised international training courses Management of District Heating Enterprises for the members of the Association. Project Training of the Staff of District Heating Enterprises, 2005-2007 In March 2005 the LDHA received assistance from the EU Social Fund for project Training of the Staff of District Heating Enterprises. The main goal of the project was to train staff to increase the competitive ness of economic operators and of the Lithuanian economy in general by developing human resources. During the implementation of the project training was provided to the staff of 107district heating enterprises according to the following four training programmes: “Management”, “Marketing”, “Financial Management and Accounting” and “EU Energy Policy”. The LDHA has recently prepared an application for the 2007-2013 EU structural financial support, following the training aids ”Development of human resources at enterprises“ of the Priority 1 ”Sufficient employment and social comprehension“ of the human resources development actions program. The goal of the training aids is to improve the knowledge and skills of employees and managing staff, and to increase their ability to adapt themselves to company needs and labor market changes.

II.10	For the largest district heating scheme in your country provide the following data (preferably for 2007).

# UAB „Vilniaus energija“

| DH delivery to 3 sectors (in GJ/year) | 2007 Residential sector GWh 1811 TJ/year 6519.6 % 70,2% Industry, commercial companies GWh 0 TJ/year 0 % 0 Public sevices (budgetary organizations) GWh 285 TJ/year 1026.0 % 11,1% Competitive consumers GWh 481 TJ/year 1731.6 % 18,7% Total: GWh 2577 TJ/year 9277.2 |
| --- | --- |
| Total length of pipeline network (in km) | 542 km |
| Residents receiving heat from DH (in persons and/or households) (residential floor space – m2) | a) Residents 5033 dweling-houses Total 7160 b) residential floor space 10 137 558 m2 |

II.11	Describe a showcase DH scheme in your country (one with outstanding qualities / innovative / new scheme for existing buildings etc.)

The district heating supply system consists of the following 3 basic parts: 1) heat source; 2) heat supply and distribution network; 3) consumer systems (see Fig. 1). Fig. 1. District heating supply system. 1 – heat source; 2 – heat supply and distribution network; 3 – consumer heating systems. Every facility producing heat energy, as boiler, heat pump, CHP plant (where the heat energy is a secondary product), geothermic or solar energy units, etc. can be considered as heat sources The heat supply and distribution network is a complex of facilities, consisting of pipelines, piping accessories, pumps, control and measuring instrumentation and other elements, by means of which the DH water (or steam) is delivered and distributed to the consumers. Nowadays for the erection of pipelines mostly pre-insulated pipes are used, which are laid down directly into soil or concrete channels (non-communicating, half-communicating or communicating channels). The pipeline network is the most expensive part of the DH supply system. As well, the pipelines are divided into a) feeders – from the heat source to every district or to the consumers with individual substations; b) distribution network – from feeders or individual substations up to the pipe branches of the buildings; c) inlet network of buildings – from the pipe branches of the distribution network (or feeders) to the inlet valves of the individual substations. The consumer heating systems consist of the equipment installed in the building substations, heating and hot water systems. The buildings may also be equipped with other systems performing heating function: cooling and air conditioning (where the heat energy is used for the air heating) and technological systems, where the heat energy is necessary for the technological process. Classification of DH supply systems. DH supply systems can be individual and district heating network type. Depending on the heat source, the district heating network type systems (DHN) are divided into CHP plants (producing simultaneously heat and power) and boiler-houses (generating only heat energy). In the individual DH supply systems the heat energy is produced in the buildings or in the heating equipment installed in buildings. 3 Fig. Diagram of the district heating of a city/town or a settelment of Lithuania 4 Fig. Underground heating network in Vilnius 5 Fig. Underground heating network in Kaunas 6 6 Fig. Map of District Heating inLithuania Heat is supplied to consumers via underground heating networks built in Lithuanian cities and towns and in the majority of the country‘s settlements.

III	HEAT MARKET

III.1	Provide your country’s total heat demand for 2007.

| Sector | In GJ |
| --- | --- |
| Residential sector | In 2007, ~61200TJ (all buildings and houses which are not in DH sector) heat was delivered to final consumers out of which ~44370 TJ was delivered to households for heating and hot water preparation purposes. The rest (about 27,5 %) was delivered to other users (industry, commercial and public services). |
| Services and other sector |  |
| Industrial sector (space heat + process heat) |  |
| TOTAL |  |

III.2 a	Provide the shares of energy sources used to satisfy heat demand in the residential + services and other sectors combined for 2007.

| Source | In % |
| --- | --- |
| District heating | 50 |
| Natural gas | we have no data |
| Electricity | we have no data |
| Oil / Petroleum products | we have no data |
| Coal | we have no data |
| Renewables and others | we have no data |
| Heat pumps | we have no data |
| Other | we have no data |
| Total | 100 |

III.2 b	Provide the same shares of energy sources used in new buildings built in the year 2007 (or the most recent year for which data is available).

| Source | In % |
| --- | --- |
| District heating | we have no data |
| Natural gas | we have no data |
| Electricity | we have no data |
| Oil / Petroleum products | we have no data |
| Coal | we have no data |
| Renewables and others | we have no data |
| Heat pumps | we have no data |
| Other | we have no data |
| Total | 100 |

III.3	Comment shortly the present situation on the market regarding the sources that customers use for space and warm water heating (so comment the data provided in question III.2).

we have no data

III.4	Provide the figure for hot water consumption in your country in litres per year or litres per capita (preferably for 2007).

~36500 litres/year per capita it is about 75-100 litres/day/per capita

VI	CHP IN ELECTRICITY PRODUCTION

VI.1 a	Provide the percentage of CHP in your country’s electricity production.

In 2007 Lithuanian public CHP plants generated 2,880 TWh of electricity (with a total installed capacity of 2592 MW) CHP plant Installed capacity, MW Disposable capacity, MW Electricity production, TWh Lithuanian PP 1800,0 1732,0 0,963 Vilnius CHP 384,0 366,0 0,745 Kaunas CHP 170,0 161,0 0,712 Mažeikiai CHP 160,0 148,0 0,242 Jonava Achema CHP 21,0 21,0 0,102 Klaipeda CHP 11,0 9,0 0,027 Panevezys CHP 35,0 33,5 0,010 Siauliai CHP 3,0 - 0,014 Petrašiunai CHP 8,0 7,0 0,004 Other CHP 0,048 Total: 2592,0 2477,5 2,880 The share of CHP electricity in general power production makes 20,6 %

# VI.1 b	Provide a short description of the situation of CHP heat autoproduction in industrial processes (outside DH).

| In Lithuania there are 11 cogeneration power plants, the heat energy of which are supplied to industrial plants, i.e. they do not belong to the district heating sector. |
| --- |
| Production for 2007 (Joule) | About 8800 TJ |
| Installed capacity (MWth) | n.a. |

VI.2	Describe the developments concerning CHP over the last five years (2002 – 2007).

In the sources of heat production (in DH sector) cogeneration facilities were erected in order to produce electricity. Throughout the 18 years of independence of Lithuania, 13 cogeneration power plants have been built/modernized in Lithuania. The biggest of them are as follows: II Vilniaus elektrinė (2006), AB “Panevėžio energija” (2008), in UAB “Litesko“ subsidiaries: “Marijampolės šiluma“ (2007), “Alytaus energija” (2008), Noreikiškių boiler house (2006), UAB “Tauragės šilumos tinklai“ (2007). The total volume of power and heat energy installed in these power plants is 62 MW and 153 MW respectively. Until 2007, 21 cogeneration power plants were built in Lithuania (in the district heating sector), with the total heat 1541 MW and power capacity 629 MW. Following the “Cogeneration development plan“ adopted by the Ministry of Economy of the Republic of Lithuania, before year 2020 about 102 cogeneration power plants are planed to be built in the Lithuanian district heating sector (79 of them will belong to district heating companies, whereas 23 will belong to other enterprises and systems), with the total power capacity from ~1133 MW to ~2331 MW (the installed power capacity will depend on the fuel – bio fuel, utility waste, other local fuels or natural gas), and heat capacity respectively from ~4000 MW to ~8200 MW.

# VI.3	Provide the fuel sources used in CHP for 2007.

| Fuel sources used for CHP | In % or GJ |
| --- | --- |
| Oil / Petroleum products | 2,3 |
| Coal and coal products | 0 |
| Natural gas | 91,2 |
| Renewables | 6,5 |
| Waste | 0 |
| Other | 0 |
| TOTAL | 100% |

VII	ENERGY MARKET

VII.1		Describe the central developments that have occurred in the energy market of your country in the last five  years (2002 – 2007). Address elements like legislation, prices, socio-economic developments etc. Also indicate what the situation was before the described developments.

Almost all information you need is answered in II.6, II.7 and II.8 questions.

VII.2	Provide an indication of the primary energy resources imports and exports in your country over the most recent period of five years (preferably 2002 – 2007).

VIII	ORGANIZATIONAL ASPECTS

VIII.1	Provide information on the national CHP/DHC association and/or the organization responsible  for completing this questionnaire.

The Lithuanian District Heating Association (LDHA) is a voluntary public organization representing the interests and rights of the Lithuanian District Heat utilities, organisations and others associated energy structures in the DH sector.

The Association is comprised of 41 members 32 are DH companies. Members of LDHA produce and supply around 98 % of the total heat through the DH network in the Republic of Lithuania, and 9 companies whose activities are closely linked to the heat sector.

Main activities:

- To represent the rights of the members, defend their interests in state, public and international organization

- To form and coordinate groups of specialist for preparation of legal and technical acts regarding development and management of DH sector.

- To provide all the necessary, legal and technical consultancy, the information on new technologies, business and managements subjects to the members;

- To arrange seminars, conferences, exhibitions.

- To establish and develop economical-technical links with international organizations and foreign partners.

- To carry all the other activities regarding promotion and development of DH/CHP in Lithuania.

The Association activities are based upon total publicity (with regard to its members), equality of members, democratic forms of management.

There are 8 employees working in the Association.

# Contact details:

# President Mr. Vytautas Stasiunas

Naugarduko g. 55a

LT-03204 Vilnius

Lithuania

Tel. +370 5 2356045

Fax. +370 5 2356044

e-mail: info@lsta.lt

www.lsta.lt

Remark: Regarding DH sector the data in this review is presented from public DH companies which supply not less than 5 GWh heat per year.

# Footnotes

Ecoheatcool Project ‘ Recommendations and project reports’, Work Package 1, p. 87 and further

Ecoheatcool Project ‘ Recommendations and project reports’, Work Package 1, p. 87 and further

Ecoheatcool Project ‘ Recommendations and project reports’, Work Package 4, p. 181 (Figure 3)

Ecoheatcool Project ‘ Recommendations and project reports’, Work Package 4, p. 183 (Figure 7)

# Text boxes

1

2

thous./MWh

3

6

1

1

1

1

Integrated DH supplyand distribution network

Heat substation

District Boiler house

1

6

1

1

1

2

1

6

3

4

5

6

6

7

Biofuel Boiler hpuse

District Boiler house

Power

Pump house

Industrial Boiler hpuse

1 Heat source

2 Integrated DH system

3 Regional boiler station

4 Local DH system

5 Local heat source

6 Consumers

7 City/town boundary

Integrated DH system

Integreated DH system rezerve

Local DH system

Local heat source

Integrated DH system

Local DH system

Pumps

Regional boiler station

Integreated DH system rezerve

Local DH system

Municipal gass

Integrated DH system

Local DH system

Supplied to the DH network

Supplied to consumers

Heat losses

Heat losses (%)

Comparative fuel input (kg.o.e./MWh)

The avarage

of temp./year

Trend

Moveing avarege 20-year period

Annal DH production – 10300 GWh

Installed capacity – 8500 MW